## Slide 1
VSS
VECTORIZED SIGNAL STAR
VSS-1
16-BIT SIMD CORE
EEE4120F · 2026
A SIMD-lite extension of StarCore-1 — twice the byte throughput, one instruction.
"For when every cycle on orbit counts."
Satellites generate floods of byte-packed sensor data — temperature channels, voltage rails, GPIO status. The baseline StarCore-1 forces you to unpack, compute, repack every word. VSS does both bytes at once, with a single new opcode and a lane-split ALU. Same pipeline. Same toolchain. Half the instruction count on the workloads that hurt most.
WHAT IT DOES
::
Dual 8-bit lanes
The ALU splits the carry chain at bit 7. Two independent byte ops, one clock.
+1
One new opcode
4'b1110 (VECTOR). 8 vector ops via funct[2:0]. Reserved 1010 untouched.
=
Zero scalar regression
vector_mode = 0 keeps every Practical 4 instruction bit-for-bit identical.
->
Drop-in datapath
Two new wires (vector_mode, funct), one new ALUOp encoding. That's the whole edit.
2x
BYTES / INSTR
6x
MODELLED SPEEDUP*
39/39
GOLDEN TESTS PASS
SPEC SHEET
ARCHITECTURE
16-bit single-cycle RISC, Harvard
VECTOR ISA
VADD VSUB VINV VSHL VSHR VAND VOR VSLT
ENCODING
opcode 4'b1110, funct = instr[2:0]
MODES
scalar 16b / SIMD-lite 2 x 8b
MODULES TOUCHED
ALU.v · ALU_Control.v · ControlUnit.v
VERIFIED ON
Icarus Verilog 12.0 + GTKWave
EEE4120F HPES Project · Group 7
Joab Gray Kloppers (KLPJOA002) · Alex Hillman (HLLALE010)
* Modelled on packed 8-bit
telemetry workloads