## Slide 1
VSS
Vectorized Signal Star
A SIMD-lite extension of the StarCore-1 RISC core
EEE4120F HPES Project · 2026
Group 7
Joab Gray Kloppers
KLPJOA002
Alex Hillman HLLALE010
MS2 TECHNICAL DEMO

## Slide 2
2 / 13
Twice the byte throughput.
One instruction.
VSS adds a single SIMD-lite extension to the Practical 4 StarCore-1: a new VECTOR opcode that splits the 16-bit ALU into two independent 8-bit lanes. Built for the byte-packed workloads embedded telemetry lives on — sensor fusion, status masks, threshold compares — where the scalar core wastes most of its cycles unpacking and repacking.

## Slide 3
3 / 13
VSS · Group 7 · EEE4120F HPES 2026
The problem with scalar on packed data
Why specialise the StarCore-1 at all?
StarCore-1 (baseline)
Two bytes packed in one register? You pay 5–8 instructions per pair.
; add packed pairs A, B
SHR R1, A, 8
AND R2, A, 0xFF
SHR R3, B, 8
AND R4, B, 0xFF
ADD R5, R1, R3
ADD R6, R2, R4
SHL R5, R5, 8
OR R7, R5, R6
8 cycles per byte-pair
VSS (this work)
One instruction, both bytes, one cycle.
; add packed pairs A, B
VADD R7, A, B
1 cycle per byte-pair
Telemetry payloads pack two ADC channels or status bytes per 16-bit word. The scalar core spends most of its life moving bits around — VSS does the actual work instead.

## Slide 4
4 / 13
VSS · Group 7 · EEE4120F HPES 2026
The StarCore-1 datapath with VSS modifications
Red signals are new for VSS; everything else is unchanged from Practical 4.
What's new
vector_mode
New 1-bit signal from Control Unit. Switches ALU between scalar and 2 × 8-bit lane mode.
ALUOp = 2'b11
New encoding (ALUOP_VECTOR). Tells ALU_Control to bypass the opcode decode table.
funct[2:0]
instr[2:0] of the VECTOR instruction; passes straight through to alu_control.
opcode 4'b1110
VECTOR instruction. R-type-like register addressing, writes ALU result back to register file.

## Slide 5
5 / 13
VSS · Group 7 · EEE4120F HPES 2026
Three modules, ~30 lines of new Verilog
The smallest possible edit that delivers a real SIMD extension.
ALU.v
Lane-split arithmetic
Dual case-statement: vector_mode = 0 keeps the original 16-bit ops; vector_mode = 1 splits a, b and result into independent {hi, lo} 8-bit lanes. The carry chain between bits 7 and 8 is broken by construction — each lane evaluates as its own 8-bit expression.
+ vector_mode input
+ 8 SIMD-lite ops
ALU_Control.v
Funct passthrough
Added one casex pattern: 6'b11xxxx → ALU_Cnt = funct. When ALUOp = 2'b11 the funct field bypasses the opcode decode table entirely. Every baseline pattern from Practical 4 is unchanged.
+ funct[2:0] input
+ ALUOP_VECTOR case
ControlUnit.v
New opcode + mode bit
Added case for opcode 4'b1110 (VECTOR): R-type-like register addressing, ALUOp = 2'b11, and assertion of the new vector_mode output. All other opcodes safely default vector_mode to 0.
+ vector_mode output
+ OP_VECTOR case

## Slide 6
6 / 13
VSS · Group 7 · EEE4120F HPES 2026
The VECTOR instruction
One opcode, eight operations, zero impact on existing instructions.
Instruction encoding (16 bits)
1110
opcode [15:12]
RS1
[11:9]
RS2
[8:6]
WS
[5:3]
funct
[2:0] → ALU op
funct[2:0] selects the vector operation
funct | Mnemonic | Behaviour (when vector_mode = 1)
000 | VADD | lane-wise add
001 | VSUB | lane-wise sub
010 | VINV | bitwise NOT of operand A
011 | VSHL | per-lane shift left (b[11:8] ¦ b[3:0])
100 | VSHR | per-lane shift right (b[11:8] ¦ b[3:0])
101 | VAND | bitwise AND
110 | VOR | bitwise OR
111 | VSLT | per-lane set-less-than (unsigned)
Reusing the ALU's existing 3-bit operation encoding for funct means ALU_Control needs no new decode logic — it just forwards the bits. Opcode 4'b1010 (the brief's reserved coprocessor slot) is deliberately left untouched.

## Slide 7
7 / 13
VSS · Group 7 · EEE4120F HPES 2026
Gold standard: software reference vs hardware DUT
Two independent implementations. If they agree, the hardware matches the spec.
Verification flow
1
Python golden model
vss_golden.py — independent reference implementation of the VSS ALU spec.
2
Test vector list
14 ALU + 16 ALU_Control + 9 ControlUnit cases, covering scalar regression and every vector op.
3
Verilog testbench
Drives the same vectors into the DUT, compares to expected values, prints PASS/FAIL.
4
VCD waveform
$dumpvars captures every signal — GTKWave shows the lane split visually.
vss_golden.py · alu_vector(a, b, op)
def alu_vector(a, b, op):
a_hi, a_lo = (a >> 8) & 0xFF, a & 0xFF
b_hi, b_lo = (b >> 8) & 0xFF, b & 0xFF
if op == ADD:
hi = (a_hi + b_hi) & 0xFF # carry trapped
lo = (a_lo + b_lo) & 0xFF # wraps in-lane
elif op == SUB:
hi = (a_hi - b_hi) & 0xFF
lo = (a_lo - b_lo) & 0xFF
...
return ((hi << 8) | lo) & 0xFFFF

## Slide 8
8 / 13
VSS · Group 7 · EEE4120F HPES 2026
Gold standard results
Hardware bit-exact against software reference across every operation.
39 / 39
tests passed
ALU_tb.v
14 / 14
ALU_Control_tb.v
16 / 16
ControlUnit_tb.v
9 / 9
0 failures · 0 warnings
vvp alu_tb.vvp
=================================================================
VSS ALU Golden-Measure Test Group 7 (KLPJOA002, HLLALE010)
=================================================================
--- Scalar mode (16-bit, baseline) ---
[1] PASS ADD-carry a=00ff b=0001 result=0100
[2] PASS SUB-borrow a=0100 b=0001 result=00ff
[3] PASS SHL4 a=0fff b=0004 result=fff0
[4] PASS SLT-true a=0005 b=000a result=0001
--- Vector mode (2 x 8-bit lanes, VSS) ---
[5] PASS VADD-basic a=0a05 b=2007 result=2a0c
[6] PASS VADD-nocarry a=10ff b=0001 result=1000 ← lane split
[7] PASS VSUB-basic a=8010 b=4002 result=400e
[8] PASS VSUB-noborrow a=2000 b=1001 result=10ff ← no borrow
... [9–14] PASS VAND VOR VSLT-mix VSHL VSHR VINV
Results: 14 PASS, 0 FAIL (out of 14 tests)
*** GOLDEN MEASURE MATCH — VSS ALU verified ***

## Slide 9
9 / 13
VSS · Group 7 · EEE4120F HPES 2026
Waveform proof: the broken carry chain
Same operands, two cycles. The signal trace makes the lane split self-evident.
Read the bottom two rows. Before the dashed line: scalar 0x00FF + 0x0001 → high byte goes from 0x00 to 0x01 (carry propagated). After: vector mode is high, 0x10FF + 0x0001 → low lane wraps to 0x00, high lane stays 0x10. No carry crosses bit 7. That single property is the whole VSS innovation.

## Slide 10
10 / 13
VSS · Group 7 · EEE4120F HPES 2026
Modelled performance vs the StarCore-1 baseline
Single-cycle ISA: instruction count is cycle count. Numbers are modelled, not measured.
Method
For each workload we count the StarCore-1 instructions needed to perform the same byte-level computation (unpack → op → repack), then divide by the VSS instruction count (1 per word).
Speedup factor printed above each pair. Range 5×–8× across these workloads.

## Slide 11
11 / 13
VSS · Group 7 · EEE4120F HPES 2026
Live demo — what we'll run now
Three commands, three minutes. Icarus Verilog 12.0 + GTKWave on this laptop.
1
vvp alu_tb.vvp
ALU gold standard
14 vectors, scalar + vector. Watch test #6 (VADD-nocarry) — that's the headline.
→ 14 / 14 PASS
2
gtkwave ALU_tb.vcd
Waveform inspection
Open vector_mode, a, b, result[15:8], result[7:0]. Zoom to the mode transition.
→ Visible lane split
3
vvp aluctrl_tb.vvp && vvp cu_tb.vvp
Control path verified
Funct passthrough on ALUOp=11 + vector_mode asserted for exactly opcode 1110.
→ 25 / 25 PASS
Roles
Alex drives slides 1–6 (motivation, system, ISA, modules) · Joab drives slides 7–11 (gold standard, waveform, performance, live demo)

## Slide 12
12 / 13
VSS, in one slide
What we built
A SIMD-lite extension of StarCore-1: one new opcode, one new mode signal, 8 vector operations sharing the existing 3-bit ALU encoding.
What we proved
39 of 39 module-level golden tests pass. Scalar regression is zero. The lane split is visible on the waveform between bits 7 and 8.
What's next
Top-level integration with the unchanged Practical 4 datapath, then memory-mapped I/O for telemetry ingest. Per-lane masks and saturation as stretch goals.
39 / 39
golden tests pass across ALU, ALU_Control and ControlUnit

## Slide 13
Thank you.
Questions?
Group 7 · EEE4120F HPES Project · 2026
Joab Gray Kloppers (KLPJOA002) · Alex Hillman (HLLALE010)